## Slide 1: Workflow PhysIO Functions
Lars Kasper
April 23, 2013

## Slide 2: General Workflow PhysIO Toolbox
The example files create the input structure for physio_main_create_regressors
This function processes all physiological logfiles.
It outputs the physiological confound regressors for the GLM.

## Slide 3: Workflow PhysIO Toolbox
Read logfiles
Preprocess physiological data
Model time series physiological noise
Of peripheral physiological data
Vendor-specific
RETROICOR
Respiratory Volume
Heart Rate
Include confound regressors (GLM)
Filter noisy ECG & detect cardiac pulses
Hand-pick missing pulses
Multiple_regressors file for SPM
SPM Matlabbatch

## Slide 4: Function List PhysIO Toolbox
physio_read_physlogfiles
physio_read_physlogfiles_GE
physio_read_physlogfiles_philips
physio_create_nominal_scan_timing
physio_create_scan_timing_from _gradients_philips
physio_get_onsets_from_locs
physio_get_cardiac_pulses
physio_find_ecg_r_peaks
physio_cardiac_detect_outliers
physio_correct_cardiac_pulses_manually
physio_findpeaks
physio_crop_scanphysevents_to_acq_window
physio_filter_respiratory
physio_create_retroicor_regressors
physio_get_cardiac_phase
physio_get_respiratory_phase
physio_downsample_phase
physio_get_fourier_expansion
physio_get_sample_points
physio_scaleorthmean_regressors
physio_orthogonalise_physiological_regressors
physio_load_other_multiple_regressors
Read logfiles
Preprocess physiological data
Model time series physiological noise
Include confound regressors (GLM)

## Slide 5: Function List PhysIO Toolbox (continued)
physio_plot_cropped_phys_to_acqwindow
physio_plot_raw_physdata
physio_plot_raw_physdata_diagnostics
physio_print_figs_to_ps
Visualization
Auxiliary/Wrappers
physio_main_create_regressors
physio_findpeaks
physio_cfg_matlabbatch

## Slide 6: Selecting the right options: Decision tree to setup physIO config file
Vendor
GE?...see next page
Synchronization of scan times and physiological logfiles
Nominal scan timing
Read Gradient timecourse to detect scans
Cardiac Data Preprocessing
None
Take pulse events from logfile
ECG
Scan finished regularly
Scan finished prematurely (hitting stop button)
Count from beginning
Model

## Slide 7: physio_main_create_regressors
physio
sqpar
thresh
verbose
log_files
model
physio_main_create_regressors
physio
verbose
sqpar
thresh
log_files
R
model
ons_secs